Assesment of the Best Practises /

Labākās prakses izvērtējums

(D26, WP4)

The sole responsibility for the content of this material lies with

the authors. It does not necessarily reflect the opinion of the European Union.

Neither the EACI nor the European Commission are responsible for any use that

may be made of the information contained therein.

Informative material elaborated by Zemgale Regional Energy Agency in close cooperation with   Initiative Wohnungswirtschaft Osteuropa, IWO e.V. on the possibilities of improval of energy efficiency of the houses, the methodology and experience, taking as basis the renovated houses in Jelgava, Latvia and Germany.

Refurbishment of buildings: Compilation of BEST PRACTICE

A best practice is a technique, method, process ore activity which conventional wisdom regards as more effective at delivering a particular outcome than any other technique, method, process, etc. when applied to a particular condition or circumstance. The idea is that with proper processes, checks, and testing, a desired outcome can be delivered with fewer problems and unforeseen complications. Best practices can also be defined as the most efficient (least amount of effort) and effective (best results) way of accomplishing a task, based on repeatable procedures that have proven themselves over time for large numbers of people.

In the following we compiled best practice as examples regarding to the energy efficiency of buildings. In the present work it is not possible to describe in detail the buildings, their condition before and after refurbishment, the used techniques and the energy effect. The examples are described in terms of material information. Detailed information can be obtained under the indicated contact data.

Energy Initiative Riga – Pilot Project of the Cities of Berlin and Riga	4

German-Latvian Environmental Pilot Project: Multi-family Building 4. Līnija 1, Jelgava	6

German-Latvian Environmental Pilot Project: Multi-family Building Helmaņa 3, Jelgava	9

High-rise residential building - Low Energy Building	12

School – focus on daylight illumination	15

School – focus on compactness	17

Laundry – use of waste heat	19

Housing estate – Replacement of district heating	20

Heat from wood chips	22

Hotel – internal thermal power station (CHP)	24

Street lighting	25

Indoor lighting	27

Energy consumption in hospitals  	29

| short name of the example | Energy Initiative Riga – Pilot Project of the Cities of Berlin and Riga |
| --- | --- |
| Main objective | Demonstration of technical feasibilty of complex energetic refurbishment of a privatised residential building without moving out the residents, implentation of a technical package of measure to reduce energy consumption by half |
| project address | Ozolciema iela 46/3, LV-1058 Rīga |
| Picture |  |
| type of building | multifamily residential building 602. series |
| year of construction | 1990 |
| year of renovation | 2001 |
| short overall description | Living area | 3,955 m² |
|  | number of storeys | 9 |
|  | number of staircases | 2 |
|  | number of flats | 72 |
|  | Gable walls | lightweight concrete, prefabricated slabs 360 mm |
|  | longitudinal walls | lightweight concrete, prefabricated slabs 230 mm |
|  | shear wall construction with bearing walls of masonry, cellar under the entire building aerated roof (cold roof), accessible, height app. 1,90 m longitudinal axis east-west-direction entrances on the north side balconies/loggias on the south side |
|  | energy supply | district heating (natural gas) |
|  | heating system | single-pipe system no thermostats no bypasses |
|  | warm water system | central with circulation |
| Measures | thermal insulation of exterior walls, d = 8 cm,  = 0,040 W/(mK), thermal insulation of ceiling to attic; d = 14 cm,  = 0,045 W/(mK), thermal insulation of cellar ceiling, d = 6 cm,  = 0,050 W/(mK), new windows; U = 1,30 W/(m²K), g = 60%, double-pipe heating, new radiators, thermostatic valves, exhaust air units, heat cost allocator, refurbishment of stairwells |
| energy consumption before renovation | Heating | 155 | kWh/(m²a) |
|  | warm water | no data |  |
| costs of refurbishment | Total | 1,656,934 847.177 | DM (2000) € |
|  | per m² | 418,95 214,21 | DM/m² €/m² |
| energy-related costs | Total | 1,139,804 582.772 | DM (2000) € |
|  | per m² | 288,19 147,35 | DM/m² €/m2 |
| Financing | subsidy by Berlin City Council (used for preparation, monitoring, construction supervision and financing the implementation works made by local companies) | 1,031,406 | DM (2000) |
|  | Subsidies from supplier of construction material | 646,107 | DM (2000) |
|  | Internal |  |  |
| energy consumption after renovation | Heating | 73 | kWh/(m²a) |
|  | warm water | no data |  |
|  | energy supply | district heating (natural gas) |
| contact details for further information | Latvijas Universitātes Fonds Basteja bulv.12, LV-1050 Rīga Dr. L. Snidere Tel:. 371 – 7227175, fax: 371 - 7228661 luf@lanet.lv |
|  | Initiative Wohnungswirtschaft Ost (IWO) e.V. Friedrichstraße 95, D-10117 Berlin Knut Höller +49 30 20679802 hoeller@iwoev.org |
|  | Senatsverwaltung für Stadtentwicklung Württembergische Straße 6, D-10707 Berlin Peter Wollschläger +49 30 90123380, peter.wollschlaeger@senstadt.berlin.de |
| website(s) illustrating the example | http://www.stadtentwicklung.berlin.de/aktuell/pressebox/archiv_volltext.shtml?arch_0011/nachricht87.html |

| short name of the example | German-Latvian Environmental Pilot Project: Multi-family Building 4. Līnija 1, Jelgava |
| --- | --- |
| main objective | Demonstration of technical feasibilty of complex energetic refurbishment of a privatised residential building without moving out the residents, implementation of a technical package of measure to reduce energy consumption by half, implementation of a financial model consisting of a combination of an investment grant and a loan taken by the residents |
| project address | 4. Līnija 1, LV-3003 Jelgava |
| picture |  |
| type of building | multifamily residential building 103. series |
| year of construction | 1980 |
| year of renovation | 2008 |
| short overall description | living area | 1,488.4 m² |
|  | number of storeys | 3 |
|  | number of staircases | 4 |
|  | number of flats | 23 |
|  | gable walls | masonry, 510 mm |
|  | longitudinal walls | lightweight concrete, prefabricated slabs 300 mm, 250 mm |
|  | shear wall construction with bearing walls of masonry, exterior walls (gable) 510 mm, interior walls380 mm cellar under the entire building aerated roof (cold roof) with height between 0,4 m…0,9 m longitudinal axis north-south-direction entrances on the east side balconies/loggias on the west side |
|  | energy supply | district heating (natural gas), combined heat an power |
|  | heating system | single-pipe system no thermostats no bypasses |
|  | warm water system | central with circulation |
| Measures | thermal insulation of exterior walls, d = 16 cm,  = 0,035 W/(mK), thermal insulation of ceiling to attic; d = 18 cm,  = 0,045 W/(mK), thermal insulation of cellar walls, d = 8 cm,  = 0,035 W/(mK), new windows; U = 1,1 W/(m²K), g = 60%, double-pipe heating, new radiators, thermostatic valves heat cost allocator refurbishment of stairwells |
| energy consumption before renovation | Heating | 241.1 | kWh/(m²a) |
|  | warm water | Included |  |
| costs of refurbishment | Total | 231,328.72 326,080.96 | Ls € |
|  | per m² | 155.42 219,10 | Ls/m² €/m² |
| energy-related costs | Total | 215,387.46 303,610.20 | Ls € |
|  | per m² | 144.71 203.98 | Ls/m² €/m² |
| Financing | subsidy by German Federal Ministry of Environment and KfW Bankengruppe | 83,838.72 118,179.06 | Ls € |
|  | subsidy by City of Jelgava | 21,740.00 30,644.70 | Ls € |
|  | bank loan taken by administrative company SIA NIP from a Latvian commercial bank and forwarded to each individual flat owner | 125,750.00 177,257.20 | Ls € |
| energy consumption after renovation | Heating | 140.6 | kWh/(m²a) |
|  | warm water | Included |  |
|  | energy supply | district heating (natural gas), combined heat an power |
| contact details for further information | SIA JNIP Jelgavas Nekustama Ipasuma Parvalde Pulkveža Brieža iela. 26, LV-3007 Jelgava, Juris Vidžis +371 63020605 info@jnip.lv |
|  | Initiative Wohnungswirtschaft Ost (IWO) e.V. Friedrichstraße 95, D-10117 Berlin Knut Höller +49 30 20679802 hoeller@iwoev.org |
|  | Ingenieurgesellschaft BBP Bauconsulting mbH Wolfener Straße 36, D-12681 Berlin Dr.-Ing. Hans-Jürgen Gaudig +49 30 93692311 gaudig@baucon.de |
| website(s) illustrating the example | www.nip.lv |

| short name of the example | German-Latvian Environmental Pilot Project: Multi-family Building Helmaņa 3, Jelgava |
| --- | --- |
| main objective | Demonstration of technical feasibilty of complex energetic refurbishment of a privatised residential building without moving out the residents, implementation of a technical package of measure to reduce energy consumption by half in accordance to the German Energy Ordinance EnEV 2007, implementation of a financial model consisting of a combination of an investment grant and a loan taken by the residents |
| project address | Kristapa Helmaņa iela 3, LV-3004 Jelgava |
| picture |  |
| type of building | multifamily residential building 104. series |
| year of construction | 1983 |
| year of renovation | 2009 |
| short overall description | living area | 1,411.60 m² |
|  | number of storeys | 5 |
|  | number of staircases | 2 |
|  | number of flats | 24 |
|  | gable walls | lightweight concrete, prefabricated slabs 300 mm |
|  | longitudinal walls | lightweight concrete and aerated concrete, prefabricated slabs 300 mm, 250 mm |
|  | shear wall construction with bearing walls of concrete, exterior walls (gable) 300 mm, interior walls 140 mm/160 mm, cellar under the entire building, aerated roof (cold roof), accessible, height 1,45 m … 2,26 m, longitudinal axis northwest-southeast-direction, entrances on the northeast side, balconies/loggias on the southwest side |
|  | energy supply | district heating (natural gas), combined heat an power |
|  | heating system | single-pipe system no thermostats no bypasses |
|  | warm water system | central with circulation |
| Measures | thermal insulation of exterior walls, d = 14 cm,  = 0,035 W/(mK), thermal insulation of ceiling to attic; d = 8 cm,  = 0,024 W/(mK), thermal insulation of cellar ceiling, d = 12 cm,  = 0,035 W/(mK), new windows; U = 1,1 W/(m²K), g = 60%, air passages in window frames for ventilation, double-pipe heating, new radiators, thermostatic valves heat cost allocator refurbishment of stairwells |
| energy consumption before renovation | Heating | 185.1 | kWh/(m²a) |
|  | warm water | 73.8 | kWh/(m²a) |
| costs of refurbishment | Total | 224,064.33 315,841.10 | Ls € |
|  | per m² | 158.73 223.75 | Ls/m² €/m² |
| energy-related costs | Total | 146,946.15 207,135.30 | Ls € |
|  | per m² | 104.10 146.74 | Ls/m² €/m² |
| financing | subsidy by German Federal Ministry of Environment and KfW Bankengruppe | 74,070.85 104,410.27 | Ls € |
|  | subsidy by City of Jelgava | 15,554.88 21,926.16 | Ls € |
|  | bank loan taken by administrative company SIA NIP from a Latvian commercial bank and forwarded to each individual flat owner | 134,438.60 189,504.65 | Ls € |
| energy demand after renovation | Heating | 88.0 | kWh/(m²a) |
|  | warm water | 35.0 | kWh/(m²a) |
|  | energy supply | district heating (natural gas), combined heat an power |
| contact details for further information | SIA JNIP Jelgavas Nekustama Ipasuma Parvalde Pulkveža Brieža iela. 26, LV-3007 Jelgava, Juris Vidžis +371 63020605 info@jnip.lv |
|  | Initiative Wohnungswirtschaft Ost (IWO) e.V. Friedrichstraße 95, D-10117 Berlin Knut Höller +49 30 20679802 hoeller@iwoev.org |
|  | Ingenieurgesellschaft BBP Bauconsulting mbH Wolfener Straße 36, D-12681 Berlin Dr.-Ing. Hans-Jürgen Gaudig +49 30 93692311 gaudig@baucon.de |
| website(s) illustrating the example | www.nip.lv |

| short name of the example | High-rise residential building - Low Energy Building |
| --- | --- |
| project address | Schulze-Boysen-Straße 35/37, D-10365 Berlin |
| picture | (photo: K. Dombrowski) |
| type of building | multifamily residential building series WHH-GT (Berlin) |
| year of construction | 1974 |
| year of renovation | 2006/2007 |
| short overall description | number of storeys | 18/21 |
|  | number of staircases | 2 |
|  | living area | 18.142 m² |
|  | number of flats | 295 |
|  | Business area | 117 m² |
|  | number of business premises | 2 |
|  | shear wall construction with bearing walls of concrete, exterior walls 260 mm with 50 mm insulation layer (prefabricated triple layer concrete slabs) ground floor with business premises and technical facilities only, aerated roof (cold roof), accessible, height 2,6 m, leaky building envelope (n50 = 5,2…8,7 h-1) |
|  | energy supply | district heating (natural gas), combined heat an power |
|  | heating system | double-pipe system no thermostats |
|  | warm water system | central with circulation |
|  | ventilation system | exhausting system |
| Measures | thermal insulation of exterior walls of the upper floors, d = 12 cm,  = 0,035 W/(mK), thermal insulation of exterior walls of the ground floor, d = 10 cm,  = 0,035 W/(mK), thermal insulation of ceiling above ground floor; d = 8 cm (inside area) and d = 10 cm (outside area),  = 0,035 W/(mK), thermal insulation of ceiling to attic; d = 14 cm,  = 0,035 W/(mK), reduction of thermal bridges, new windows; upper floors: U = 1,1 W/(m²K), U = 1,3 W/(m²K), g = 47%, ground floor: U = 1,5 W/(m²K), g = 55%, ventilation system with heat recovery ( = 73%), internal thermal power station, new radiators with thermostat valves, new pipes (cold and warm water, waste water) and wiring, energy saving lamps in all public areas, tiling of bathrooms and kitchens, new apartment entrance doors, renovation of unrented apartments, renovation of stairwells and hallways, refurbishment of lift systems, repair of business premises and replacement of façade elements, new entrance building with concierge |
| energy demand before renovation (primary energy) | heating | 96,6 | kWh/(m²a) |
|  | warm water | included |  |
| costs of refurbishment | total | 9,108,752 | € |
|  | per m² | 499,00 | €/m² |
| energy-related costs | total | app. 4,400,800 | € |
|  | per m² | app. 244,50 | €/m² |
| financing | 1. standard funding by German KfW-Bank (CO2-reduction program) | app. 150 | €/m² |
|  |  | app. 2,586,000 | € |
|  | 2. additional funding by German KfW-Bank | app. 50 | €/m² |
|  |  | app. 907,400 | € |
|  | 3. additional funding by German KfW-Bank for ventilation system with heat recovery | app. 50 | €/m² |
|  |  | app. 542,000 | € |
|  | credit interest of 1,96 % p.a., duration of 20 years |
|  | subsidy by partial reduction of credit (15% of 1.-3.) | 660,000 | € |
|  | 4. standard funding by German KfW-Bank (program modernisation of housing space) | app. 4,400,000 | € |
|  | credit interest of 3,98 % p.a., duration of 20 years |
|  | internal | 800,000 | € |
| energy demand after renovation (primary energy) | heating | 44,9 | kWh/(m²a) |
|  | warm water | included |  |
|  | energy supply | district heating(natural gas) combined heat an power and internal thermal power station |
|  | renewable energy | heat recovery system |
| contact details for further information | HOWOGE Wohnungsbaugesellschaft mbH Ferdinand-Schultze-Straße 71, D-13055 Berlin Angela Reute +49 30 54642401 pr@howoge.de |
|  | IPB B Ingenieurbüro für Projektentwicklung und Baubetreuungs GmbH Spinolastraße 28b, D-13125 Berlin Ralf Hillenberg +49 30 2789420 info@ipbb.de |
|  | ISB Ingenieurgesellschaft Schneider & Bauer mbH Planungsbüro für Haustechnik Rheinsteinstraße 14, D-10318 Berlin Jörg Schneider +49 30 55489313 info@isb-berlin.de |
| website(s) illustrating the example | www.neh-berlin.de www.howoge.de |

| short name of the example | School – focus on daylight illumination |
| --- | --- |
| project address | Friedrich-Ebert-Schule Staatliche Regelschule 8 Langer Graben 19, D-99092 Erfurt |
| picture | (photo: final report by Fraunhofer-ISE) |
| type of building | school, series WBS 70, prefabricated building |
| year of construction | 1974 |
| year of renovation | 1995-1997 |
| short overall description | number of storeys | main building: 4 connecting section: 3 annex building: 3 |
|  |  | gym not in the project |
|  | gross floor area | 4,134.0 m² |
|  | heated net area | 3,944.0 m² |
|  | envelope | 5,394.1 m² |
|  | heated volume | 14,436.6 m³ |
|  | compactness A/Ve | 0,37 m-1 |
|  | students & teachers | 173 |
|  | exterior walls 260 mm with 50 mm insulation layer (prefabricated triple layer concrete slabs) exterior wall of connecting section with asbestos containing material, wooden windows with insulation glazing, district heating, double-pipe system with 5 heating circuits, manual controlled radiators, classrooms with free aeration, some rooms (special class rooms, kitchens, toilets) with wall or roof vents, bad natural lighting: shadowing is needed for no glaring, this leads to more use of electric light, insufficient illumination with daylight |
| Measures | thermal insulation of exterior walls, d = 10 cm, thermal insulation of roof (sloping insulation), d = 10 cm, application of heat protection glazing; north: Ug = 0,9 W/(m²K), Uw = 1,2 W/(m²K), south: Ug = 1,3 W/(m²K), Uw = 1,5 W/(m²K), thermal insulation of cellar wall, d = 8 cm, various decentralized ventilation systems: transverse ventilation with exhaust fan, ventilation system with heat recovery ( = 73%), free aeration, daylight concept: combination of shadowing, light control, reflection and refraction, new heating service station, heating system with room-by-room temperature control, reduced indoor temperatures: class rooms: from 24°C to 20…21°C, hallways, stairwells and toilets: to 18°C |
| energy demand before renovation | heating | 143,6 | kWh/(m²a) |
|  |  | district heating |  |
|  | electric energy | 17,4 | kWh/(m²a) |
| costs of refurbishment | total | 2,892,000 1,478,656 | DM € |
|  | per m² | 733 375 | DM/m² €/m² |
| energy-related costs | total | 2,489,000 1,272,605 | DM € |
|  | per m² | 631 323 | DM/m² €/m² |
| financing | internal | 1,215,000 621,220 | DM € |
|  |  | 308 157 | DM/m² €/m² |
|  | subsidy by German Federal Environment Ministry (58%) | 1,677,000 857,436 | DM € |
|  |  | 425 217 | DM/m² €/m² |
| energy demand after renovation | heating | 54,3 | kWh/(m²a) |
|  | electric energy | 10,5 | kWh/(m²a) |
|  | energy supply | district heating |
| reward | Thuringian Energy Saving Award 2000 |
| contact details for further information | Stadt Erfurt Amt für Grundstücks- und Gebäudeverwaltung Löberwallgraben 19, D-99096 Erfurt Karl Mülders; +49 361 6553609 grundstueck-gebaeude@erfurt.de |
|  | Fraunhofer-Institut für Solare Energiesysteme ISE Heidenhofstraße 2, D-79110 Freiburg Dr. Christel Russ; +49 761 45880; christel.russ@ise.fhg.de |
| website(s) illustrating the example | www.erfurter-schulen.de/schulen/rs8/ www.eneff-schule.de |
| short name of the example | School – focus on compactness |
| project address | Bertolt-Brecht-Gymnasium Lortzingstraße 1, D-01307 Dresden |
| picture | (photo: final report by Fraunhofer-IPB) |
| type of building | School |
| year of construction | 1967 |
| year of renovation | 1993-1995 |
| short overall description | number of storeys | 3 |
|  |  | before | after |
|  |  | renovation |
|  | gross floor area | 4,134 m² | no data |
|  | heated net area | 3,807 m² | 4,523 m² |
|  | main area | 2,407 m² | no data |
|  | envelope | 6,750 m² | 6,870 m² |
|  | heated volume | 14,999 m³ | 20,810 m³ |
|  | compactness A/Ve | 0,45 m-1 | 0,33 m-1 |
|  | number of classrooms | 20 + 6 |
|  | standard classroom | 50 m², 20…25 students |
|  | disadvantageous geometry, relation between envelope and volume, exterior walls gable: light weight concrete, longitudinal: excelsior between concrete wooden windows with insulation glazing, district heating, thermostatic controlled radiators, class rooms with free aeration, sufficient illumination with daylight |
| Measures | transformation of two patios into atria with glass-roofs, Uw = 1,6 W/(m²K), g = 59%, improving the compactness, thermal insulation of exterior walls, d = 12 cm,  = 0,040 W/(mK), thermal insulation of roof, d = 15 cm,  = 0,040 W/(mK), new windows, Uw = 1,5 W/(m²K), g = 58%, thermal insulation of cellar wall, d = 8 cm,  = 0,040 W/(mK), thermal insulation of cellar bottom, d = 8 cm,  = 0,040 W/(mK), new heating system and control, connecting classrooms with atria for preheating the air, free aeration through atria roofs for improve temperature conditions during summertime |
| energy demand before renovation | heating | 283 | kWh/(m²a) |
|  |  | district heating |  |
| costs of refurbishment | total | 4,783,000 2,445,509 | DM € |
|  | per m² | 1,057 540 | DM/m² |
| energy-related costs | total | insufficient data | DM |
|  | per m² | insufficient data | DM/m² |
| financing | internal | insufficient data | DM |
|  |  | insufficient data | DM/m² |
|  | subsidy by German Federal Economy Ministry | insufficient data | DM |
|  |  | insufficient data | DM/m² |
| energy demand after renovation | heating | 69 | kWh/(m²a) |
|  | energy supply | district heating |  |
|  | electric energy | 77% reduction |  |
| contact details for further information | Technische Universität Dresden Institut für Bauklimatik Zellescher Weg 17, D-01069 Dresden Uwe Meinhold +49 351 46333756 uwe.meinhold@tu-dresden.de |
|  | Landeshauptstadt Dresden – Schulverwaltungsamt Fiedlerstraße 30, D-01307 Dresden S. Jahn +49 351 4889284 schulverwaltungsamt@dresden.de |
| website(s) illustrating the example | www.eneff-schule.de |

| short name of the example | Laundry – use of waste heat |
| --- | --- |
| project address | Neue Arbeit Mönchengladbach GmbH Tomphecke 31, D-41169 Mönchengladbach |
| picture | (photo: http://neuearbeit.info/neue-arbeit) |
| type of building | industrial building |
| year of construction | 2003 |
| year of renovation | new building |
| short overall description | number of storeys | 3 |
|  | effective area | 4.500 m² |
|  | of that office area | 700 m² |
|  | capacity | 100 t/week |
|  | employees | 100 |
|  | laundry lines equipped with energy-optimizers, waste heat used for heating the laundry, part of waste heat is stored in an underground tank (60 m³) 700 m² office spaced heated with in-floor heating, auxiliary heating not required, aeration via underground channels, cooling via well, solar power system (100 m² of modules), serving also as shadowing, |
| energy demand | natural gas | 750 | MWh/a |
|  | electric energy | 55 | MWh/a |
| energy savings compared to | in total 25 | % |
| investment | in total | 10,000,000 | € |
| contact details for further information | EnergieAgentur.NRW Kasinostraße 19-21, D-42103 Wuppertal Gerald Orlik +49 202 24552-33 gerald.orlik@ea-nrw.de |
| website(s) illustrating the example | www.ea-nrw.de |

| short name of the example | Housing estate – Replacement of district heating |
| --- | --- |
| project address | Prae-Bau-Siedlung D-44359 Dortmunde-Mengede |
| pictures | (http://www.praebausiedlung.de/staedtebau.html) |
| type of building | multifamily residential buildings |
| year of construction | 1961…1964 |
| year of renovation | 2003…2004 |
| short overall description | number of buildings | 18 |
|  | number of storeys | 4 |
|  | living area | 25.757 m² |
|  | number of flats | 350 |
|  | construction of prefabricated concrete slabs, insufficient thermal insulation of building envelope, need of modernization of kitchens, baths and balconies, district heating (natural gas), obsolete boilers, insufficient insulation, leaky pipes, decentralized water heating (electrical and natural gas), |
| Measures | thermal insulation of exterior walls, thermal insulation of roofs, new windows with heat protection glazing, replacement of obsolete boilers, installation of two thermal power stations with Pth = 384 kW and Pel = 240 kW (65% fulfilment of heat demand), Pth = 1,890 kW installation of two low-temperature boilers for fulfilment of peak load, 3,000 m of new district heating pipes, 46 new heat transfer stations, centralized water heating with circulation, new heated hot water tanks in ground floors |
| costs of refurbishment | total | 13,200,000 | € |
|  | per m² | 512 | €/m² |
| energy-related costs | total | insufficient data | € |
|  | per m² | insufficient data | €/m² |
| financing | internal | insufficient data | € |
|  |  | insufficient data | €/m² |
|  | funding by German KfW-Bank (CO2-reduction program) | insufficient data | € |
|  |  | insufficient data | €/m² |
| savings | energy | 39 | % |
|  | CO2 | 50 | kg/(m²a) |
| contact details for further information | Stefan Leuchten, EnergieAgentur.NRW +49 0221 86642-285 stefan.leuchten@ea-nrw.de |
|  | DOGEWO Dortmunder Gemeinnützige Wohnungsgesellschaft mbH Landgrafenstraße 77, D-44139 Dortmund +49 231 1083-0 mail@dogewo21.de |
| website(s) illustrating the example | www.ea-nrw.de www.mein-haus-spart.de www.dogewo21.de |

| short name of the example | Heat from wood chips |
| --- | --- |
| project address | Entsorgungsbetrieb Stadt Dorsten Postfach 21 02 65 ,D-46269 Dorsten |
| pictures | (http://www.energieagentur.nrw.de) |
| type of building | industrial building & fire house |
| year of installation | 2004 |
| initial situation | natural gas boilers of Entsorgungsbetrieb Stadt Dorsten (disposal service) in need of rehabilitation, insufficient heat output for additional vehicle hall, |
| concept | project target: stable heating cost local heat supply system, heat supply for building of Entsorgungsbetrieb Stadt Dorsten and new fire house, thereby investment for separate heating system, with flue gas evacuation and natural gas supply as well as maintenance in new fire house not necessary, wood chips are available by local forest tending |
| remarks | for small heating systems (dwelling houses) are to prefer pellets, because of higher caloric value, wood chips are less expensive, but need more storage space, handling, transport and technical equipment are costlier, funding and lower fuel cost compensate higher investment |
| short technical description | good accessibility for trucks and all-season heat demand (water heating for showers) are good premises for wood chips fired plant base load 300 kW thermal output, per year 1.100 m³ wood chips are needed (≈ 370 t of wood), for peak load a natural gas boiler with 900 kW thermal output is added, heat storage tank with 10 m³, heated by wood chips boiler, primary function is to heat up the buildings at morning |
| energy demand | wood chips | 30 | m³/week |
| savings | fuel cost compared to natural gas | 11,300 | €/a |
|  | natural gas | 100,000 | m³/a |
|  | CO2 | 240.000 | kg/a |
| financing: subsidy of 35 % of investment by special programm of Nordrhein-Westfalen |
| contact details for further information | EnergieAgentur.NRW Kasinostraße 19-21, D-42103 Wuppertal +49 202 24552-30 info@ea-nrw.de |
|  | Cosanne Ingenieure GmbH Drubbel 7-9, D-46286 Dorsten +49 236 998820 info@cosanne.de |
| website(s) illustrating the example | www.ea-nrw.de |

| short name of the example | Hotel – internal thermal power station (CHP) |
| --- | --- |
| project address | Landhotel Voss Winterberger Straße 36, D-57368 Lennestadt-Saalhausen |
| picture | (photo: http://www.hotel-voss.de) |
| type of building | hotel |
| year of construction | 1691 1977 (heating system) |
| year of renovation | 2004 |
| short overall description | number of storeys | 3 |
|  | beds | 50 |
|  | special equipment | indoor swimming pool, sauna, solarium |
|  | natural gas boilers in need of rehabilitation, project target: cost cutting, internal thermal power station, variable engine speed makes partial load operation possible, base load of electric energy can be produced by CHP, except of winter season the whole heat demand can be covered by CHP, |
| energy out put | thermal | 14…39 | kW |
|  | electrical | 8…20 | kW |
|  | energy costs | 7,500 | €/a |
| savings | CO2 | 65,000 | kg/a |
| investment | in total | 70,000 | € |
| financing | subsidy by German KfW-Bank (environmental program) | 30,000 | € |
| contact details for further information | EnergieAgentur.NRW Kasinostraße 19-21, D-42103 Wuppertal Matthias Kabus +49 202 24552-31 matthias.kabus@ea-nrw.de |
| website(s) illustrating the example | www.ea-nrw.de |

| short name of the example | Street lighting |
| --- | --- |
| project address | Neuenkirchen-Vörden |
| picture |  |
| before | 77 cantilever lights |
|  | High Pressure Mercury Vapour Lamp (HME), each 2 x 125 W |
| after | 77 cantilever lights |
|  | High Pressure Sodium Vapour Lamp (HST), each 1 x 70 W |
| savings | energy | 58,828 | kWh/a |
|  |  | 70 | % |
|  | CO2 | 36,000 | kg/a |
|  | cost | 8,824 | €/a |
| project address | Regensburg, historic city |
| picture |  |
| before | 10 historic lights |
|  | High Pressure Mercury Vapour Lamp (HME), each 80 W conventional ballast |
| after | 10 historic lights |
|  | LED-modules, retrofit, each 42 W electronic ballast light management |
| savings | energy | 1,520 | kWh/a |
|  |  | 42 | % |
|  | CO2 | 930 | kg/a |
|  | cost | 228 | €/a |
| project address | Streets of Bohmte |
| picture |  |
| before | 800 post lights |
|  | High Pressure Mercury Vapour Lamp (HME) mix of 80 W and 120 W conventional ballast |
| after | 800 top light lanterns |
|  | compact fluorescent lamp, each 2 x 18 W electronic ballast |
| savings | energy | 220,818 | kWh/a |
|  |  | 70 | % |
|  | CO2 | 135,100 | kg/a |
|  | cost | 33,123 | €/a |
| project address | Bispingen, Main Street |
| picture |  |
| before | 63 cantilever lights |
|  | High Pressure Mercury Vapour Lamp (HME), each 2 x 80 W |
| after | 84 post lights |
|  | High Pressure Sodium Vapour Lamp (HST), each 1 x 70 W |
| savings | energy | 19,684 | kWh/a |
|  |  | 40 | % |
|  | CO2 | 12,000 | kg/a |
|  | cost | 2,952 | €/a |
| contact details for further information | licht.de Lyoner Straße 9, D-60528 Frankfurt am Main +49 69 6302-353 licht.de@zvei.org |
| website(s) illustrating the example | www.licht.de |

| short name of the example | Indoor lighting |
| --- | --- |
| project address | Hamburg, Hochbahn AG |
| picture |  |
| before | 987 lights: down lights drop lights, recessed luminaires, desk lights |
|  | fluorescent lamps (T5), partial electronic ballast |
| after | 956 recessed luminaires with micro-lensing optics |
|  | fluorescent lamps (T5), each 2 x 28 W electronic ballast light management |
| savings | energy | 129,164 | kWh/a |
|  |  | 57 | % |
|  | CO2 | 79,000 | kg/a |
|  | cost | 23,250 | €/a |
| project address | Berlin, sports hall Free University of Berlin |
| picture |  |
| before | 104 grid lamps |
|  | fluorescent lamps (T8), each 2 x 58 W low-loss ballast |
| after | 56 reflector grid lamps |
|  | fluorescent lamps (T5), each 3 x 80 W electronic ballast light management |
| savings | energy | 10,360 | kWh/a |
|  |  | 35 | % |
|  | CO2 | 6,300 | kg/a |
|  | cost | 1,865 | €/a |
| project address | Grammar school of Sundern |
| picture |  |
| before | 376 grid lights |
|  | fluorescent lamp (T8), each 2 x 58 W conventional ballast |
| after | 564 grid lights |
|  | fluorescent lamp (T5), each 1 x 35 W electronic ballast light management |
| savings | energy | 60,597 | kWh/a |
|  |  | 81 | % |
|  | CO2 | 37,100 | kg/a |
|  | cost | 10,907 | €/a |
| project address | City hall of Menden |
| picture |  |
| before | 608 grid lights |
|  | fluorescent lamp (T8), each 4 x 18 W conventional ballast |
| after | 152 drop-lights directly above workspace |
|  | fluorescent lamp (T5), each 2 x 80 W electronic ballast light management |
| savings | energy | 134,526 | kWh/a |
|  |  | 83 | % |
|  | CO2 | 82,300 | kg/a |
|  | cost | 24,215 | €/a |
| contact details for further information | licht.de Lyoner Straße 9, D-60528 Frankfurt am Main +49 69 6302-353 licht.de@zvei.org |
| website(s) illustrating the example | www.licht.de |

| short name of the example | Energy consumption in hospitals |
| --- | --- |
| short overview of content | research project, supported by the Deutsche Bundesstiftung Umwelt (DBU), energy consumption in 20 hospitals with capacity of 300…600 beds was analysed, examination was concentrated on energy-relevant sectors where consumption could be measured and influenced by technical measures first step: collection and compilation of detailed information about operation modes and energy consumption, measured data revealed opportunities to optimize operations and formed the basis for evaluating energy efficiency of the energy supply, annual energy consumption of various sectors was analyzed and energy cost calculated, comparison of hospitals energy use based on key data, saving options were also developed for the various sectors along with best practice solutions, cost and savings were estimated, key data and simple tools for approximate calculation were developed, key data and energy costs can be used for comparison purposes |
| short preview of results | replacement of old, inefficient facilities leads to remarkable energy savings and is economically efficient, new facilities do not guarantee optimized energy consumption, when operational mode is inefficient, key figures are necessary to identify saving potentials, offer the opportunity to select suitable measures, allow to proof the success of such measures |
| energy saving potentials in different sectors |
| heat supply | energy and storage management: replacement of low-temperature boiler by condensing gas boiler or district heating supply, substitution of indirect water heating and hot water storage for heat storage tank in heating circuit and direct water heating adjustment of system temperatures to requirements, insulation of pipes |
|  | energy saving potential | ≈ 10…20% | thermal energy |
| hot water supply | see energy and storage management |
| ventilation | control of volume flow in line with demand (except intensive care unit), low flow velocity in wide ducts, short ducts with few change of direction, efficient ventilator with level of efficiency of 0,6…0,65, filters with pressure monitoring, |
|  | energy saving potential | ≈ 10% | electrical energy for ventilation |
| cooling | new magnetically pivoted turbo refrigerating machine for base load, operation in combination with existing machines |
|  | energy saving potential | ≈ 50% | cooling energy |
| elevators | new elevator, frequency controlled gearless machines minimized friction losses by adequate lubrication and replacement of bearings intelligent control to prevent empty runs, “sleep mode” during night time, substitution of old drives for new ones with higher level of efficiency (> 0,8), optimized weight balance, cabin lights with energy saving lamps, automatically turn off when not in use, display board with LED, automatically turn off when not in use |
|  | energy saving potential | ≈ 75% | electrical energy for operation |
| contact details for further information | Fraunhofer-Institut für Umwelt-, Sicherheits- und Energietechnik UMSICHT Osterfelder Straße 3, D-46047 Oberhausen Carsten Beier +49 208 8598-1416 carsten.beier@umsicht.fraunhofer.de |
| website(s) illustrating the example | www.umsicht.fhg.de |

# Footnotes

http://en.wikipedia.org/wiki/Best_practice

## 1 Latvian Lats = 1,4096 €

Sources:	http://www.neh-berlin.de/

www.ise.fraunhofer.de/veroeffentlichungen/nach-jahrgaengen/2000/sanierung-der-staatlichen-regelschule-08-in-erfurt-unter-verwendung-von-tageslichtelementen/at_download/file

Petzold, K. et al.: Energetische Sanierung und energieökonomische Erweiterung unter Verbesserung des sozial-kulturellen und des pädagogisch-funktionellen Niveaus von Typenschulbauten, Phase II, Schlussbericht. Berlin, Dresden, Stuttgart, November 1998

http://www.licht.de/fileadmin/09_Roadshow_Special/Roadshow_Best-Practice_Beispiele.pdf

http://www.licht.de/fileadmin/09_Roadshow_Special/Roadshow_Best-Practice_Beispiele.pdf

Fraunhofer-Institut für Umwelt-, Sicherheits- und Energietechnik UMSICHT; Beier, C., final report: analysis of energy consumption and generic best-practice solutions for relevant sectors of consumption in hospitals, June 2009

Fraunhofer Institute for environmental, safety and energy technology UMSICHT; annual report 2009-2010